## Slide 1: A QUickLook Determination of Oil-in-place in Oil Shale Resource plays
Marlan W. Downey, Julie Garvin, RC Lagomarsino, David F. Nicklin

## Slide 2: Acknowledgements:
Roxanna Oil and Gas Company
  Eddie Little
Matador Resources Company
  Anne Lindsey McColloch
  Justin Bagley
  Bo Henk

## Slide 3: Discussion Topics
Gas-in-place measurements in the Coal and Shale Gas Industry
  Gas desorption methodology
Importance of Hydrocarbon Target Volumes in Unconventional Resource Plays
  Measure amount of Hydrocarbons available
  Application of RockEval Pyrolysis for S1 values

## Slide 4: Gas Desorption Methodology
Standard analytical technique over 20 years
  Measures total gas contained in coal cores or shale cores.
  Allows the determination of the total gas resource in place in a given area.

## Slide 5: Hydrocarbon Target Volumes
Focus on application of hydrocarbon distillation from Rock-Eval.
  Requires rock samples, preferably whole core, properly collected.
  Determines volumes of distillable hydrocarbons in the rock in mg of hydrocarbon/g of dry rock.
  Relatively simple and cheap to do.
  Results can be obtained early in exploration campaign.
  Easily up-scaled to reflect total rock potential.

## Slide 6: Hydrocarbon Target Volumes
Emphasis on S1 measurement of distillable hydrocarbons.

## Slide 7
S1 Peak
Volatilization of existing HC
S2 Peak
Pyrolysis of kerogen
(nonvolatile organic matter)
Existing Oil
TEMPERATURE
Rock Eval Pyrolysis
S1 represents the free hydrocarbons in a rock
  Primarily indicates generated free oil (liquid hydrocarbons)
  The greater the S1 value, the greater amount of free oil
  Optimum data from whole core
Tmax
Potential Oil
TIME

## Slide 8: APPLICATION ProceDURE
Establish S1 values, preferably from whole core, preferably every foot. This represents measured oil-in-place per unit volume of rock.
Upscale oil-in-place to Acre-feet or “Section-feet” (i.e. one square mile of surface area x one foot thick x hydrocarbon richness).
Resulting volume from core measurements is a minimum value for the oil-in-place volume.

## Slide 9: Methodology: Oil in Place from S1
MS1HC= Ah (ρAv) (S1Av)(.001) ÷ 8.11E-10 acre-ft/cc
Where:
MS1HC = Mass of S1 hydrocarbons per section (g)
A = Area of interest in acres (sectional area – 640 acres)
h = Reservoir height (ft)
ρAv = Average bulk density (g/cc)
S1Av =Average S1 (mg/g)
Step 1: grams of oil per section

## Slide 10: Methodology (cont.)
VS1HC = MS1HC ÷ ρoil
Where:
VS1HC = Volume of S1 hydrocarbons per section (cc)
MS1HC = Mass of S1 hydrocarbons per section (g)
ρoil = Density of oil (g/cc)
Step 2: volume of oil per section (cc)

## Slide 11: Methodology (cont.)
Oil in Place per section (Bbl)
=
VS1HC x 6.29E-6 bbl/cc
Step 3: barrels of oil per section

## Slide 12: Oil in Place from S1
Oil in Place per 640 acre/ft = 4965.36 x (ρAv) (S1Av)/(ρoil)
Where:
ρAv = Average bulk density (g/cc)
S1Av =Average S1 (mg/g)
ρoil = Density of oil (g/cc)
Simplified Equation

## Slide 13: Oil in Place from S1
Oil in Place per 640 acre/ft = 15922.78 x (S1Av)
Where:
S1Av =Average S1 (mg/g)
  Assumes:
  2.5 g/cc Bulk Density
  50º API Oil Gravity
Simplified Equation

## Slide 14: Conversions
1 section = 640 Acres
1 cc = 8.10713194 E-10 Acre-ft
1 cc = 6.28981077E-6 Bbl
Specific gravity = 141.5/(131.5 + API gravity)
Specific gravity 1 =1 g/cc
1 mg = .001 g

## Slide 15: Quicklook Conversion of S1 to Oil
Using S1 in mg/g to BBL of Oil in 640 acres/foot
0.0
1.0
2.0
3.0
4.0
8,000
24,000
40,000
56,000
72,000
S1
MG/G
BBL/FT
(Min. Target Vol.)
Assumes:
2.5 g/cc Bulk Density
50º API Oil Gravity
(R.C. Lagomarsino)

## Slide 16
OIL FAIRWAY
DRY GAS FAIRWAY
COMBO
LIQUIDS/GAS
FAIRWAY
Well ‘A’
Well ‘B’
Eagle Ford Shale – STUDY Wells

## Slide 17
Vertical Variations in S1 Values for Eagle Ford, Well ‘A’
Chart: S1 Data vs Depth, Ro= 0.7 to 0.8
| 2.19 | 0.47000000000000008 | 2.88 | 2.65 | 3.9 | 3.8299999999999987 | 2.72 | 3.01 | 2.4499999999999997 | 3.19 | 2.3899999999999997 | 2.68 | 2.2999999999999998 | 3.17 | 1.3800000000000001 | 1.51 | 0.54 | 0.67000000000000082 | 2.9899999999999998 | 3.69 | 4.6199999999999966 | 6.6599999999999975 | 7.13 | 6.63 | 4.72 | 5.76 | 1.48 | 4.8899999999999997 | 4.1599999999999975 | 5.85 | 6.72 | 6.37 | 4.7 | 3.4099999999999997 | 2.4699999999999998
S1 Data | 7704.25 | 7722.1 | 7752.9 | 7755.4 | 7762.5 | 7764.65 | 7770.65 | 7779.2 | 7782.75 | 7784.75 | 7791.85 | 7794.15 | 7800.7 | 7802.7 | 7809.7 | 7815.25 | 7818.3 | 7821.3 | 7827.2 | 7833.1 | 7839.2 | 7846.5 | 7848 | 7853.9 | 7861.3 | 7864.2 | 7866.15 | 7872.5 | 7875.5 | 7878.75 | 7881.85 | 7884.35 | 7887.35 | 7891.35 | 7896.1
Average S1 = 3.55 g/mg
56.525 MBBL/640 ac/ft
(Less Thermally Mature)
Weighted Avg. = 11.0
MMBBL/640 Ac.
(Min. Target Vol.)

## Slide 18
OIL FAIRWAY
DRY GAS FAIRWAY
COMBO
LIQUIDS/GAS
FAIRWAY
Well ‘A’
Well ‘B’
Eagle Ford Shale – STUDY Wells

## Slide 19
Vertical Variations in S1 Values for Eagle Ford, Well ‘B’
Chart: S1 Data vs Depth, Ro= 1.2 to 1.4
Average S1 = 1.86 g/mg
29.616 MBBL/640 ac/ft
Weighted Avg. = 4.0
MMBBL/640 Ac.
(Min. Target Vol.)
(More Thermally Mature)

## Slide 20
Rock-Eval S1 value provides early measurement of oil in place.
Can be up-scaled easily for various thicknesses for quantified values of oil-in-place.
Measurements of oil-in-place compared to production decline analysis will provide improved measures of recovery efficiency.
For further information, check out:
www.roxannaoil.com
Conclusions